In Gel Digestion for Coomassie Stained Bands

- Washing

  - Excise bands, cut as close to the band as possible to minimize excess gel material and cut into 1mm cubes.  Place in Eppendorf tube.

  - Wash with H2O twice.

  - To gels add 100µL of ddH2O and Incubate at RT for 15min.

  - Pull off H2O and add 250µL of 50/50 ACN/H2O.  Incubate at RT for 15min.

  - Pull off solution and add 250µL of ACN.  Incubate until the gel pieces are clear.

  - Pull off solution and add 250µL 100mM ammonium bicarbonate and incubate at RT for 15min. Add 250 µL ACN and incubate at RT for 15min.  Incubate at RT for 15min.

  - Repeat step (f) 3 times to clear the stain completely. IF NEEDED YOU CAN STOP HERE AND INCUBATE OVERNIGHT (O/N).

  - Pull off solution and dry samples in speed vac for approximately 15min (must be very dry).

- Alkylation

  - Remove samples from speed vac and let cool.

  - Add 250µL of 10mM DTT/100mM ammonium bicarb and incubate at 56◦C for 45min.

  - Remove samples and let cool.

  - Pull off solution and immediately add 250µL 55mm Iodoacetamide/ 100mM ammonium bicarb (just make a 100mg/mL solution of Iodoacetamide in 100mM ammonium bicarb and dilute 10x).  Incubate at RT for 30min in the dark.

  - Pull off solution and wash with 250µL of 100mM ammonium bicarb.  Incubate at RT for 5min.

  - Add 250µL of ACN to make a 1:1 solution and incubate at RT for 15min.

  - Pull off solution and dry gel pieces in speed vac for 15min.

- Digestion

  - Add 50uL (enough to cover pieces) of Trypsin solution

    - Trypsin solution:

      - 2µL 1M CaCl2 + 50µL 1M ammonium bicarb + 945µL H2O

      - Take 100µL of the above solution and add 12.5µL of 0.1µg/µL Trypsin.

        - If doing more than 2 samples, take an extra 100µL of (1) and double the amount of Trypsin added.

  - Incubate at 4◦C for 45min then transfer tubes to 37◦C and incubate O/N.

  - Pull supernate and transfer to a new Eppendorf tube (SAVE).  To gel add 20µL of Gel Extraction Buffer (1% FA, 2% ACN, in H2O) and incubate for 20 min at room temp. Add 20µL ACN to make a 1:1 solution.  Incubate at RT for 15min. Pull off supernatant and add to the saved tube.

  - Repeat (c) 2x. Gel pieces can now be discarded.

  - Dry the pooled samples in speed vac until dry. Put in -20◦C freezer until ready to MS.  Add 20µL 5% FA when ready for MS analysis.